## Slide 1: ST Hackathon(Result) Geninus-SKKU
Heesoo Kim
Kyuran Lee
Doeon Gu
Yeonju Lee
2024.08.22

## Slide 2: Background : Xenium + Visium HD
Visium HD
18,085gene
(whole transcriptome)
Bin
16, 8, 2 um binning
Xenium in situ
422 gene
Multimodal
segmentation
(Single cell resolution)
Whole transcript
Single cell
Integration Visium HD and Xenium
 Whole transcriptome & single cell resolution
at spatial level

## Slide 3: Workflow
Xenium DAPI Image + Visium HD H&E image  Affine matrix  transformation of xenium coordinate
Segmentation of Visium HD (nuclei, boundary)
Xenium annotation w/morphology
Xenium  Visium HD deconvolution(8, 16, nuclei, boundary)
Integration of Visium HD and xenium
Evaluation of integration V and X
Downstream analysis  cell-cell interaction, GSEA
Image alignment
Xenium coord
transformation
integration
Xenium  Visium HD deconvolution
Result of integration
Evaluation
Downstream analysis
Visium HD
segmentation
Xenium DAPI
+
Visium HD H&E
By affine matrix
Nuclei / boundary
Deconvolution Visium HD
(by xenium)
8μ vs 16μ vs nuclei vs boundary
Xenium annotation
(by canonical marker)
Gene correlation
Cell-cell interaction
Min distance approach

## Slide 4: 1. Image alignment of Xenium DAPI + Visium HD H&E
-0.02483 | 1.28649 | -48408.9
-1.28649 | -0.02483 | 86488.58
0 | 0 | 1
Manually image alignment of Xenium DAPI and Visium HD H&E in xenium explorer.
Transformation of Xenium um to Visium HD pixel coordinate using Affine matrix.
Successful transformation between two different image using the affine matrix.
Xenium to Visium
Xenium um coordinate
Visium HD pixel coordinate
Transformed xenium coordinate
-0.015 | -0.77702 | 66477.27
0.777019 | -0.015 | 38911.85
0 | 0 | 1
Visium to Xenium
Inverse Matrices

## Slide 5: 2. Segmentation of Visium HD (nuclei, boundary)
Nuclei
Boundary
Xenium multimodal segmentation result
270,978 nuclei
Mean 6 bins
246,933 cells
Mean 14 bins
Non max supression
*Remove doublet
*Detection of nuclei using StarDist
Custom binning
Nuclei segmentation
Boundary segmentation
Applying boundary segmentation results in a 2.33-fold increase in bin count(2 um).

## Slide 6: 3. Xenium annotation
UMAP2
UMAP1
Xenium In Situ, Sample P5 CRC
422 features * 234,944 cells
Canonical marker-based annotation reflects morphology well in spatial mapping results in xenium data.

## Slide 7: 4. Xenium  Visium HD deconvolution(bin level)
Deconvolution
Visium HD (16um)
Visium HD (8um)
NA Singlet
15,035 121,000
11%
NA Singlet
238,084 303,884
44%

## Slide 8: 4. Xenium  Visium HD deconvolution(segment level)
NA TRUE
170,306 100,672
63%
NA TRUE
88,842 158,091
36%
 | 16 um | 8 um | Boundary | Nuclei
deconvolution % | 89% | 56% | 64% | 37%
bin count | 64 | 16 | 14 | 6
mean feature | 1010 | 311 | 402 | 208
mean count | 1759 | 432 | 591 | 273
Deconvolution
Visium HD
Left :(Nuclei Segmentation ; Visium HD H&E image)
Right : (Boundary Segmentation ; Xenium multi modal)
Low count and low features cause deconvolution failure.
Boundary segment captures more transcripts and genes than 8 µm, showing its high sensitivity.

## Slide 9: 5. Location-based integration of Visium HD and Xenium
Nuclei
Boundary
 | 0 | 1 | 2 | 3 | 4 | 5 | 6
8 um | 62.46 | 30.18 | 6.73 | 0.59 | 0.03 | 0.001 | 0.000185
Nuclei | 54.88 | 37.67 | 6.89 | 0.49 | 0.06 | 0.002 | 0.004797
Boundary | 6.57 | 87.61 | 5.58 | 0.23 | 0.01 | 0 | 0
*Cell %
Boundary segments exhibit the highest rate of matching with single cells, being the closest to single-cell resolution.
Max point
Min point
2um
Cmax distance
min(Cmin + Cmax distance) & Cmin distance ≒ Cmax distance  Centroid bin
min(bin-xenium nucleus distance) < 2 um(boundary, 8) or 4 um(nuclei)
4um
87,064 nuclei
183,011 cells
Cmin distance

## Slide 10: Discussion
Limitation
Insight
Visium HD : 8 µm, Nuclei Segment: Low sensitivity and bin counts; does not reveal single cells. Nuclei Segment: Data loss. (90%) Xenium-Boundary Segment: Provides the highest single-cell resolution and sensitivity.
 Propose the Location-based Integration
Xenium DAPI image and Visium HD H&E image that do not perfectly align. (different sections)